## Slide 1: Pune Urban Data Exchange Datathon Pollution exposure challenge
RASPP Team
Team members:
Ritesh Kalbande, Abirlal Metya, Shahana Bano, Praveen Kumar, Pooja Pawar

## Slide 2: DESIGN
We have considered the IITM AQM stations as the benchmark for comparing and obtaining the missing data points in the Climo AQM sensors.
Once the data imputation part was done, Climo AQM sensors data was used for the spatial interpolation and obtaining the PM2MAX and PM2MIN values for the given test points.

## Slide 3: ALGORITHM OVERVIEW
The Climo and IITM sensors data is obtained through the links as well as by using the pyIUDX python code which was provided.
The IITM data, which was given in the form of AQI was converted to PM2.5 concentration values using the air quality index formula.
The Climo and IITM data is developed into a hourly format. The IITM data gaps are filled either by gradient method or by using the lowest neighbor value.

## Slide 4
The Climo data gaps (original plus the gaps created after making hourly dataset) were filled based on the trends observed in the nearby IITM stations (chosen based on distance as well as similarity in emission sources for the region).
The obtained hourly Climo dataset is then used for spatial interpolation using the “nearest” interpolation method after comparing the output with other methods, again by making use of the meshgrid interpolation part of the pyIUDX code.

## Slide 5: INNOVATION HIGHLIGHTS
The highlight which probably makes this work different is the data gap filling part for Climo sensors which was done using the IITM AQM station data. There were 2 prominent reasons for using the IITM data. The variation in PM2.5 data from IITM stations and that from the Climo sensors followed a similar pattern (the concentration however being different), and also that, since the IITM AQM stations are well maintained, the data quality aspect helps in trusting the variation in PM2.5 bringing us closer to actual values during spatial interpolation.

## Slide 6
As mentioned earlier, the selection of a specific IITM AQM station for filling gaps in a Climo sensor data was done based on the distance of the 2 stations, as well as the similarity in the emission sources for 2 regions
For eg. IITM Katraj for PMPML Katraj, Rajashri Shahu bus stand, Chandani square; IITM Lohgaon for BRTS Vishrantwadi, Ambedkar soceity; IITM Bhumkar for Bremen circle, Khadki Church railway station, etc.

## Slide 7: TRAINING AND TESTING
During spatial interpolation, different methods like “cubic”, “linear”, “Rbf” were used apart from the “nearest” spatial interpolation method which we found to provide the best results for the available data.
For the data imputation part, the gradient method was tried(instead of using IITM data) to fill the original gaps in Climo sensors, but comparison with the IITM data method proved out to give better results than simple gradient method.

## Slide 8: FUTURE IMPROVEMENTS
For various reasons, we were unable to add the IITM data points for the spatial interpolation part, which we believe can further improve the accuracy of values estimation.
Including different meteorological data based on the season can add to the improvement in the results as well.

## Slide 9: THANK YOU